# Chapter 3 Installation and wiring

The followings explain the installation precautions are wiring for system reliability.

3.1 Installation Precautions

1) Make sure that the module be firmly connected to the base unit.

2) Follow the specifications of the unit for operating environment.

3) Be sure to check that the driver is corrected correctly to the connector.

4) Do not mount/dismount the module or the connector for driver while the power is

being turned on.

5) When installing the module in a closed location use a heat prevention fan as possible.

3.2 Wiring

3.2.1 Wiring precautions

- The cable length from the positioning module to the connected driver should be as

short as possible (1 to 3 M)

2) When wiring I/O signal wires, separate the wires from the power line or circuit lines.

(20 cm or more)

3) The connection cable length should be short as possible.

3.2.2 Wiring I/O signal wires

- If it is thought that there’s noise sources when wiring between the positioning module

and drivers, use the twisted pair cable and shielded cable for input pulses from the

positioning module to drivers.

2) When running I/O signal wires in piping, this should be guarded.

3) Use a stabilized external power supply (5VDC, 24VDC)

3.2.3 External connection

[ G6F-POPA ]

# 3.3 Interface with external devices

## 3.3.1 Electrical specifications

- Input specification

a) General input – upper, lower, zero point and emergency stop

| Items | Specifications |
| --- | --- |
| Standard input voltage | DC + 24 V (-15% + 20%) |
| Standard input current | 10 mA |
| On guarantee voltage | Min. DC 16 V |
| Off guarantee voltage | Max. DC 4 V |
| On delay time | less than 2 ms |
| Off delay time | less than 2 ms |

b) Phase Z input

| Items | Specifications | Response Time |
| --- | --- | --- |
| Open Collector Input | DC + 24 V (-15% + 20%) | less than 0.1 ms |
| Line Drive Input | Am26LS31 or equivalent |  |

* Other items are the same with specifications for general input.

c) Manual Pulse Input

| Items | Specifications |
| --- | --- |
| Input Voltage | DC + 5V (±5%) | DC + 5V (±5%) |
| On Guarantee Voltage | Min. DC 4V | Min. DC 8V |
| Off Guarantee Voltage | Min. DC 1V | Max. DC 2V |
| Pulse bandwidth | more than 1 ms |

- Output (NPN Open Collector)

(Pulse output section (FR, RP)

| Items | Specifications |
| --- | --- |
| Max. Open/Close Current | DC + 24V / 150mA |
|  | DC + 5V / 150mA |
| Min. Open/Close Current | DC + 24V / 2mA |
|  | DC + 5V / 2mA |
| On Max. Voltage Drop | less than 0.8V |
| Off Current Leakage | less than 0.1mA |
| External Power Supply | DC + 24 V (-15% + 2%) |
|  | DC + 5 V (+ 5%) |

# Text boxes

## REMARK

The high level of z input Phase must keep it’s status more then 0.1ms, else G6F-POPA

module may miss the input signal