Chapter6. THE FUNCTION BLOCK (GLOFA-GM)

This.chapter explain the usage of various function block, whitch is use in GWWIN to control position as to user’s determine

( A kind of function block

| No | Item | G3F-POPA | G4F-POPA | G4F-POPB | G6F-POPA | Function explain |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Module Imform- ation | POSP_CRD | POSP_CRD | POSB_CRD | POSP_CRD | Read current operation status (code) |
| 2 |  | POSP_SRD | POSP_SRD | POSB_SRD | POSP_SRD | Read current operation status ( bit ) |
| 3 | Auto matic oper ation | POSP_AST | POSP_AST | POSB_AST | POSP_AST | Start |
| 4 |  | POSP_INT | - | POSB_INT | POSP_INT | linear interpolation start |
| 5 |  | POSP_ORG | POSP_ORG | POSB_ORG | POSP_ORG | Start Returning to orgine point |
| 6 | Manual operation | POSP_INC | POSP_INC | POSB_INC | POSP_INC | Inching operation |
| 7 |  | POSP_JOG | POSP_JOG | POSB_JOG | POSP_JOG | Jog operation |
| 8 |  | POSP_RTP | POSP_RTP | POSB_RTP | POSP_RTP | Retrun to prior position to manual operation |
| 9 |  | POSP_MPG | - | POSB_MPG | - | Enable operation with manual pulse generater |
| 10 | Teaching | POSP_TEA | POSP_TEA | POSB_TEA | POSP_TEA | Target position adress teaching |
| 11 |  | POSP_VLT | POSP_VLT | POSB_VLT | POSP_VLT | Target operating speed teaching |
| 12 | Auxiliary operation | POSP_MOF | POSP_MOF | POSB_MOF | POSP_MOF | Turn off M code singal bit |
| 13 |  | POSP_VCG | POSP_VCG | POSB_VCG | POSP_VCG | Change operation speed |
| 14 |  | POSP_NM | POSP_NM | POPB_NM | POSP_NM | Continouse operation |
| 15 |  | POSP_OR | POSP_OR | POPB_OR | POSP_OR | Speed Override |
| 16 |  | POSP_SMC | POSP_SMC | POPB_SMC | POSP_SMC | Assinge operation step number |
| 17 |  | POSP_STP* | POSP_STP* | POSB_STP | POSP_STP | Decelation stop |
| 18 |  | POSP_TMP | POSP_TMP |  |  |  |
| 19 | Error | POSP_EMG | POSP_EMG | POSB_EMG | POSP_EMG | Internal emergency stop |
| 20 |  | POSP_OFF | POSP_OFF | POSB_OFF | POSP_OFF | Output-inhibited cancellation |
| 21 |  | POSP_RES | POSP_RES | POSB_RES | POSP_RES | Error reset |
| 22 | etc | POSP_FLT | POSP_FLT | POSB_FLT | POSP_FLT | Set floating point |
| 23 |  | POSP_PRE | POSP_PRE | POSB_PRE | POSP_PRE | Present point reste |
| 24 |  | - | - | - | POSP_PRM | Parameter change |

6.1 Regist Function Block for positioning in GMWIN

Positioning Function Bock can be registed accord to the next procedure.

.

Choice

Choice

6.2 The function block for reading module imformation

6.2.1 Status code read   (Status Code Read  :POSP_CRD)

Read the current position adress,operating speed,M code value,operating data numer to use the imformation in user application program or monitoring it

| Function Block type | Item | Vari able Name | Data type | contents |
| --- | --- | --- | --- | --- |
|  | Input signal | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” changed to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Level detection) |
|  |  | BASE | USINT | (Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | (Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate If you operate X-axis then assigne “0”, Y-axis then assinge “1” |
|  | Out put | DONE | BOOL | (A bit signal prove this function operated without any problem It has “1” value when the function block was operated without any problem,”0” the function block was not operated casue Some abnormal data was set at the input data part or posotining module has some truble in hardware |
|  |  | STAT | USINT | ( Display error code Display the error code when the function block has a truble while it is exctued |
|  |  | CA | DINT | ( Display the current position address |
|  |  | CV | UINT | ( Display the current position speed |
|  |  | MCD | USINT | ( Display the currnt M code number |
|  |  | CDN | UINT | ( Display the current data number |

6.2.2. Stauts bit read  (Status Bit Read  :  POSP_SRD)

Read the current position status(Bit) to monitor more detailedly or use it in user application program .

| Function Block type | Item | Variable Name | Datatype | contents |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” changed to “0→ 1”,then the function block will be operated while CPU is kept on( “0->1” : Level detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | (Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal prove this function operated with out any problem It has “1” value when this function block was operated with out any problem,”0” the function block was not operated casue Some abnormal data was set in input data part or posotining module has some truble in hardware |
|  |  | STAT | USINT | ( Display the error code Display the error code when this function block has a truble while it is exctued |
|  |  | ST1 | BOOL [ARRAY] |  |
|  |  | ST2 | BOOL [ARRAY] |  |
|  |  | ST3 | BOOL [ARRAY] |  |
|  |  | ST4 | BOOL [ARRAY] |  |
|  |  | ST5 | BOOL [ARRAY] |  |
|  |  | ST6 | BOOL [ARRAY] |  |

| Remark |  |
| --- | --- |
| The output variables(“ST1~ST6”) of “POSP_SRD” function block are very useful and must be use in user program to control positioning system with normal |

6.2.3 Auto start  (Auto Start  :  POSP_AST)

Only one step of the positioning data operated by excuting “POSP_AST” one time, and if positioning opertation completed then output variable “ACT” is truned on( Bit : ”1”) automactically

| Function Block type | Item | Variable Name | Datat ype | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Reqest the function block to be operated In case the condition of variable assinged at “REQ” changed to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal being excuted It has “1” value when this function block is being operated without any problem,”0” the function block was not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT | USINT | ( Display the error code Display the error code when this function block has a truble while it is exctued |
|  |  | ACT | BOOL | (Display the operation axis It has “1” value when this function block was operated with out any problem,at the same time make the bit status of output variable “Done” be “0” |

| Remark |  |
| --- | --- |
| Relation between output variable “ACT” and “DONE” 2) Precaution when using “POSP_AST” function block Only usable “POSP_AST” function block when opsitioning opertaion completed(The stauts of “BUSY” singal off) |

6.2.4 Linear interpolation opertaion   (Linear Interpolation  :  POSP_INT)

The function block to operate linear operation with a postioning module for control two axis

| Function Block type | Item | Variable Name | Datat ype | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  | Output | DONE | BOOL | (A bit signal being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT _X | USINT | (Display the error code of X-axis |
|  |  | STAT _Y | USINT | (Display the errror code of Y-axis |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POSP_INT” function block Only usable “POSP_INT” funcion block when opsitioning opertaion completed (The stauts of “BUSY” singal off) Available opertaion mode are single operation, repeat operation,auto operation |

6.2.5 Return to origne opint  (Origin  :  POSP_ORG)

Operation command to find the machin’s origine point by origine point return processing method accroding to the orgine parameter defined in POSPACK softawre

If return to origine opint is terminated without any problem, the return to orgine opint completion signal will be turned “on”

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Output | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

6.3. Manual opertaion

6.3.1 Inching   (Inching  :  POSP_INC)

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation” |
|  |  | ROT | BOOL | (Select the dirction of inching operation “0” : Forward / “1” : Revers |
|  |  | INCH _AMT | USINT | (Set the travle vaule of inching operation Setting range : 1∼ 99 (Unit : Pulse) |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

6.3.2 JOG operation  (JOG  :  POSP_JOG)

This function block is useful to check the position system for checking out, if there is some problem in connection signal cable between position module and servo driever or Setting positioning parameter and make pulse out by manual operating

The pulse out operation will be excuted while the condition of the variable of “Request” is kept “ON” and it change into “OFF” then  the pulse output operation will be stopped

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Level detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | ROT | BOOL | (Select the dirction of inching operation “0” : Forward / “1” : Revers |
|  |  | HL | BOOL | ( Select the speed of jog operation “0” : Low speed “1” : high speed |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display error code Display error code when this function blcok has a truble while it is exctued. |

6.3.3 Return to prior position to manual opertation (Return To Position  :  POSP_RTP)

Return to position function block is useful, When the stop point adress changed by manual operating and want it

Return to prior opsition to manual operation

( Manual operation means “Inching operation”,”Jog operation”,” MPG operation” )

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the functionblock is not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

6.3.4 Approval of Manual pulse generator   (Manual Pulse Generator : POSP_MPG)

Enable to be used attached external manual pulse generator(MPG). This funcion block must be registed and excuted in user’s program before use MPG.

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display error code Display error code when this functionblock has a truble while it is exctued. |

6.3.5 Position teaching    (Teaching  :  POSP_TEA)

Chage target position address of the special numer of positing data as to user’s define without using “POSPACK’ software

| Function Block type | Item | Variable Name | Datatype | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Reqest the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | ST_S ET | UINT | (Set the step number of data parameter to be teached Setting range : “0 ~ 299” |
|  |  | PRES ET | DINT | (Set the position address Setting range : “-16,744,447 ∼ 16,744,447” |
|  |  | MODE Remark[1] | BOOL | (Select position teaching type “0” : RAM teaching / “1” : ROM teaching |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |

| Remark |  |
| --- | --- |
| [1] The input variable “MODE” is only use with “G6F-POPA” ▶ The poision address teaching function block can be operated only after opsitioning operation completed ▶The deference between “RAM” and “ROM” teaching RAM teaching : The teaching data is not stored in positioning data parameter so repowred the PLC system, the teaching data is cleard and operating with the data set in POSPACK ROM teaching : The teaching data is stored in opsitioning data parameter even if repowred the PLC system, the teaching data is still exist |

6.3.6 Velocity teaching  (Velocity  :  POSP_VLT)

It is use for user to set the random speed value to specific data number

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | VEL_ NO | USINT | ( Set the step number of data parameter to be teached Setting range : “0 ~ 127” |
|  |  | VEL_ SET | UINT | ( Set the targrt operation speed Setting range : 1 ∼ 20,000 (Unit : X 10Pulse) |
|  |  | MODE Remark[1] | BOOL | (Select position teaching type “0” : RAM teaching / “1” : ROM teaching |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input data part or positioning module has some truble in hardware |
|  |  | STAT _X | USINT | (Display the error code of X-axis |
|  |  | STAT _Y | USINT | (Display the errror code of Y-axis |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time.. |

| Remark |  |
| --- | --- |
| [1] The input variable “MODE” is only use with “G6F-POPA” |

6.4 The function block for clear the error

6.4.1 Cancellation of output inhibition   (Pulse Out Inhibit , Off  :  POSP_OFF)

It is use to cancle the pulse out inhibit status cause by detecting uppper limit sensor,  lower limit sensor or external emergency signal

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |

6.4.2 Error reset    (Reset  :  POSP_RES)

It is use to reset if an error is ocurrented by setting data over the setting range in parameter or something during operating

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has truble while it is exctued. |

6.5 Auxiliary funtion block

6.5.1 Floating point set     (Floating, Point Set  :  POSP_FLT)

Without excuting mechanical return to orgine point f, define the present position opint as origine opoint and after Excuting “POSP_FLT” function block the current positioning address will be changed to the origine point address

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→ 1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set in input variable part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POSP_FLT” function block. (1) It can be excuted only when the positoning is completed (“ Busy : OFF”) |

6.5.2 present point Preset     (Preset  :  POSP_PRE)

It is use to change the present point addredd to the new one as to user’s define

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | PRES ET | DINT | ( Set the new address setting range : -16,744,447 ∼ 16,744,447 |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set in input variable part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POSP_PRE” function block. (1) It can be excuted only when the positoning is completed (“ Busy : OFF”) |

6.5.3 M code off      (M Code Off  :  POSP_MOF)

It can be use to turn off the M code bit signal when the signal is on ,if M code has been set to with or after mode at parameter of each axis

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Rquest the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |

6.5.4 Velocity change    (Velocity Change  :  POSP_VCG)

It can be use to change the operation speed at constant speed druing operation

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Rquest the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | VEL_ SET | UINT | (The Value of new velocity Setting range : 1 ∼ 20,000 (Unit : X 10Pulse) |
|  | Output | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has truble while it is exctued. |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POSP_VCG” function block (1) It is only usable when the positioning speed is constant ( Busy : “on”) (2) It can be use that the operation mode is selected assingle, repeat, auto operation and also jog(high speed),return to origine opint(high speed) (3) It is availbale for constant operation only with “G4F-POPB,G6F-POPA” |

6.5.5 Continuous operation    (Next Move  :  POSP_NM)

This is use for continuous operation from present operation number to the next operation step number at a random point of time without stop, if continuous operation mode is applied

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Reqest the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input variable part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POPA_NM” function block It can be use only when the speed of position is constant (Not use it in terms like accelation or deceletion of speed) (2) It can be use only at contunious mode,and can’t be at other operating mode |

6.5.6 Speed override  (Override  :  POSP_OR)

This function block is use to chage the operating speed by setting the ration on original operating speed only while the velocity of positioning is constant

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | OVR | USINT | (Set the ration on orignail valocity of positioning Setting range : 1 ∼ 15 (Unit: 10%) ex) Setting value : 12 / origine valocity : 500pps ( Changed valocity = orgine valocity X 120%, So the changed valoicity is 600pps |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input data part or posotining module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POPS_OR” function block It can be use only when the speed of position is constant(Not use it in terms like accelation or deceletion of speed) |

6.5.7 Assginment of oprtation data number   (Set Move Data Number Change  : POSP_SMC)

It is use to select the operating data number to be excuted at the next “start positioning” instruction

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | ST_S ET | UINT | ( Set the data number Setting range : “0 ∼ 299” |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function Block is not being operated casue Some abnormal data was set in input variable part or positioning module has some truble in hardware |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

| Remark |  |
| --- | --- |
| Precaution when using “POSP_SMC” function block. (1) It can be excuted only when the positoning is completed |

6.5.8 Deceletion stop   (Stop  :  POSP_STP)

It is use to temporarily stop the operation of positioning

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  | Out put | DONE | BOOL | (A bit signal that the function block is being excuted It has “1” value when this function block is being operated without any problem,”0” the function block is not being operated casue Some abnormal data was set at the input variable part or positioning module has some truble in hardware |
|  |  | STAT _X | USINT | (Display the error code of X-axis |
|  |  | STAT _Y | USINT | (Display the errror code of Y-axis |
|  |  | ACT | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time |

6.5.9 Internal emergency stop    (Emergency  :  POSP_EMG)

It is use to stop positioning data opertation instantly at emergency state, and to restart the operation that it is essential to

Excute “POSP_OFF” and “POSP_ORG” function block before excute “POSP_AST” agine

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on ( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  | Output | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |

6.6 Parameter change

6.6.1 Parameter wirte  (Parameter Write G6F-POPA:POSP_PRM)

Change biasic parameter ( Acceleration and deceletion time, jog hi-speed, return to origne opint hi speed and change M code mode ) by using function block without “POSPACK” software package

| Function Block type | Item | Variable Name | Data type | Content |
| --- | --- | --- | --- | --- |
|  | Input | REQ | BOOL | (Request the function block to be operated In case the condition of variable assinged at “REQ” change to “0→1”,then the function block will be operated while CPU is kept on( “0->1” : Rising edge signal detection) |
|  |  | BASE | USINT | ( Regist the base number Set the base number,whitch positioning module is mounted on |
|  |  | SLOT | USINT | ( Regist the slot number Set the slot number,whitch positioning module is mounted on |
|  |  | AXIS | USINT | (Assinge the axis to operate “0”: X-axis operation / “1” : Y-axis operation |
|  |  | AT | UINT | (Set the aceletion time Setting range : 1 ∼ 999(Unit: 10㎳) |
|  |  | DT | UINT | (Set the deceleration time Setting range : 1 ∼ 999(Unit: 10㎳) |
|  |  | JSH | UINT | (Set the JOG high speed Setting range : 1 ∼ 20,000(Unit : X 10pps) |
|  |  | HSH | UINT | (Set the return to origine point high speed Setting range : 1 ∼ 20,000( Unit: X 10pps ) |
|  |  | MMD | USINT | ( Set the M Code mode “0” : With / “1” : After / “2” : None |
|  | Out put | DONE | BOOL | (A bit signal prove the function block is operated without any problem When the function block is completed sucessfully, it has “1” untill the next excution time. |
|  |  | STAT | USINT | (Display the error code Display the error code when this function block has a truble while it is exctued. |

| Remark |  |
| --- | --- |
| 1) Precaution when using “POSP_PRM” function block. (1) It can be excuted only when the positoning is completed (“ Busy : OFF”) |

# Text boxes

Project (P)

Insert liberay (I)

G6F– POPA

Special.6fb

INCH

_AMT

ROT

■ Press the addtion icon then the next windows will be appear

DONE

ACT

STAT

POS((INC

AXIS

SLOT

CV

CDN

MCD

DONE

CA

STAT

POS((CRD

AXIS

DONE

ACT

STAT

POS((AST

AXIS

SLOT

BASE

REQ

AXIS

SLOT

BASE

REQ

①

① : Function block excuted by “REQ”

(first)

② : Completion of the function block

③ : Function block excuted by “REQ”

(second)

REQ

ST6

③

②

ACT

DONE

MMD

HSH

JSH

DT

DONE

STAT

POS((PRM

AT

SLOT

BASE

REQ

MODE

MODE

DONE

STAT

POS((EMG

SLOT

BASE

REQ

STAT

_Y

ACT

BASE

REQ

VEL(

SET

DONE

STAT

_Y

STAT

_X

POS((VLT

VEL(

NO

SLOT

BASE

REQ

PRES

ET

ST(S

ET

DONE

STAT

POS((TEA

AXIS

SLOT

BASE

REQ

STAT

_X

ACT

DONE

POS((TMP

AXIS

SLOT

BASE

REQ

ST5

ST2

ST4

ST3

DONE

ST1

STAT

POS((SRD

AXIS

SLOT

BASE

REQ

| Bit number | ST1 Contents | ST2 Contents | ST3 Contents |
| --- | --- | --- | --- |
| [0] | In dwell (Bit:On) | Upper limit sensor detection(Bit:On) | Unused |
| [1] | In decelation (Bit:On) | Lower limit sensor detection (Bit:On) | Display pulse output direction Froword(Bit:Off),Revers(Bit:On) |
| [2] | In steady speed (Bit:On) | Emergency stop detection (Bit:On) | ZONE#1(Bit:On) |
| [3] | In acelation (Bit:On) | Pulse output inhibited (Bit:On) | ZONE#2(Bit:On) |
| [4] | at stop state (Bit:On) | Inching operation finished(Bit:On) | ZONE#3(Bit:On) |
| [5] | In returning to origine point (Bit:On) | Position adress teaching finished (Bit:On) | Repeat operation completion(Bit:On) |
| [6] | In positioning (Bit:On) | In jog opertation at low speed(Bit:On) | Start positioning completion (Bit:On) |
| [7] | In interpolation operation (Not use in “G4F-POPA”) | In jog operation at high speed (Bit:On) | M code On(Bit:On) |
| Bit number | ST4 Contents | ST5 Contents(Terminal signal) | ST6 Contents |
| [0] | In orgine point complement(Bit:On) | Change mode speed to positioning (Use only with “G6F-POPA”) | Unused |
| [1] | In backlash compensation(Bit:On) (Not ues with “G6F-POPA”) | External upper limit signal (Bit:Off) | Error |
| [2] | In Next Move (Bit:On) | External lower limit signal (Bit:Off) | Position passing |
| [3] | In speed overriding (Bit:On) | External near zero point signal (Bit:On) | In positioning operation (Busy) |
| [4] | Unused | External orgine point signal (Bit:On) | Positioning completetion |
| [5] | In decelation stop and stop finish(Bit:On) | Unused | Return to origine point completion |
| [6] | Operation speed teching finish(Bit:On) | Unused | Return to origine point uncompletion |
| [7] | Speed change completion(Bit:On) | External emergency stop signal(Bit:Off) | Unused |

ST(S

ET

DONE

ACT

STAT

POS((SMC

AXIS

SLOT

BASE

REQ

AXIS

OVR

DONE

ACT

STAT

POS((OR

AXIS

SLOT

BASE

REQ

AXIS

SLOT

DONE

STAT

POS((JOG

HL

ROT

BASE

REQ

ACT

DONE

STAT

_Y

STAT

_X

POS((INT

SLOT

BASE

REQ

DONE

DONE

STAT

POS((RES

AXIS

SLOT

BASE

REQ

DONE

ACT

STAT

POS((PRE

PRES

ET

SLOT

BASE

REQ

DONE

ACT

STAT

POS((ORG

AXIS

SLOT

BASE

REQ

DONE

ACT

STAT

POS((RTP

AXIS

SLOT

BASE

REQ

DONE

STAT

POS((OFF

SLOT

BASE

REQ

ACT

STAT

POS((NM

AXIS

SLOT

BASE

REQ

VEL(

SET

DONE

STAT

POS((MPG

AXIS

SLOT

BASE

REQ

DONE

ACT

STAT

POS((FLT

AXIS

SLOT

BASE

REQ

DONE

ACT

STAT

PO(((VCG

AXIS

SLOT

BASE

REQ

DONE

STAT

POS((MOF

AXIS

SLOT

BASE

REQ