1.Features

- GLOFA DeviceNet module (G4L-DUEA, G6L-DUEA, GOL-DSQA, GOL-DSIA)

supports ODVA (Open DeviceNet Vendor Association) standard specification.

- Max. 63 slave station (Max 2048 points) can be controlled 1 master module.

- Station no(Mac Address) and transmission speed (baudrate) can be selected

by switch on module

- Various slave that provided by other maker can be connected to GLOFA DeviceNet

master module (G4L-DUEA / G6L-DUEA)

- Digital I/O

- Actuator

- Limit Switch

- Photo Sensor

- Inverter

- Position Controller

- A/D, D/A Converter

- GLOFA DeviceNet slave module (GOL-DSQA, GOL-DSIA) can be connected to

master module that provided by other maker

- Max. 2 master module can be installed in main base

2. Specification

2-1 Performance Specification

|  | Description |
| --- | --- |
| Topology | Linear Bus (Power & Signal on the same network cable) |
| Max. no of station | 64 station |
| No. of points | Max. 2048 points / slave |
|  | Max. 2048 points / master module |

| Transmission Speed | Distance (Thick / Thin cable) | Drop length |
| --- | --- | --- |
|  |  | 1 drop | Cumulative |
| 125 kbps | 500 / 100m | 6m | 156m |
| 250 kbps | 250 / 100m | 6m | 78m |
| 500 kbps | 125 / 100m | 6m | 39m |

3. System Configuration

3-1. In case that GLOFA works as master

3-2. In case that GLOFA works as slave

4. Name of Parts

4-1. G4L-DUEA

4-2. G6L-DUEA

※Mode Setting

| Module | Switch | Setting | Master / Slave |  |
| --- | --- | --- | --- | --- |
|  |  | SW1 | SW2 |  |  |
| G4L-DUEA G6L-DUEA |  | OFF | OFF | Master |  |
|  |  | ON | OFF | Slave (Server) |  |

| Module | Switch | Setting | Baudrate |  |
| --- | --- | --- | --- | --- |
|  |  | SW3 | SW4 |  |  |
| G4L-DUEA G6L-DUEA |  | OFF | OFF | 125 kbps |  |
|  |  | ON | OFF | 250 kbps |  |
|  |  | OFF | ON | 500 kbps |  |
|  |  | ON | ON |  |  |

4-3. G0L-DSQA

| ( Station no. switch | 0 ~ 63 (Decimal display) |
| --- | --- |
| ×10 | 10 unit |
| ×1 | 1 unit |
| ( LED Display | Communication status display |
| PWR | Power status |
| MS | Interface status |
| NS | Network status |
| ( Mode switch | Baudrate setting |
| 1:Off 2:Off | 125 kbyte |
| 1:On 2:Off | 250 kbyte |
| 1:On/Off 2:On | 500 kbyte |
| ( LED Display | Out put display |
| G0L-DSQA | 16points |

| ( Connector | 5-PIN connector |
| --- | --- |
| CON1 | DeviceNet connector |

| ( Terminal Block |  |
| --- | --- |
| G0L-DSQA | 0 ~ 15 | Output terminal block |
|  | COM1 ~ COM4 | Common (4Point Common) |
|  | NC |  |
|  | 24V | +24VDC IN |
|  | 24G | -24VDC IN |

4-4. G0L-DSIA

| ( Station no. switch | 0 ~ 63 (Decimal display) |
| --- | --- |
| ×10 | 10 unit |
| ×1 | 1 unit |
| ( LED Display | Communication status display |
| PWR | Power status |
| MS | Interface status |
| NS | Network status |
| ( Mode switch | Baudrate setting |
| 1:Off 2:Off | 125 kbyte |
| 1:On 2:Off | 250 kbyte |
| 1:On/Off 2:On | 500 kbyte |
| ( LED Display | Input display |
| G0L-DSQA | 16points |

| ( Connector | 5-PIN connector |
| --- | --- |
| CON1 | DeviceNet connector |

| ( Terminal Block |  |
| --- | --- |
| G0L-DSQA | 0 ~ 15 | Input terminal block |
|  | COM1 ~ COM4 | Common (4Point Common) |
|  | NC |  |
|  | 24V | +24VDC IN |
|  | 24G | -24VDC IN |

5. Example

5-1. System Configuration

5-2. Test Data Flow

5-3 High Speed Link Parameter (Master Station / GM4)

Even if AB Flex I/O (1794-ADN / 1794-0816 / 1794-1816) has 16points input and output, this slave

module occupies 32points (4bytes) input and output.

5-4 High Speed Link Parameter (Slave Station / GM6)

# Text boxes

# Caution

GLOFA DeiveNet system requires …..

- GLOFA GMWin : Ver. 3.3 or higher

- GLOFA GM4 CPU : Ver 2.3 or higher

- GLOFA GM6 CPU : Ver 1.3 or higher

# PWR

# CPU

Inverter

# DeviceNet

# OUT

# IN

# PWR

# CPU

# DeviceNet

# OUT

# IN

OMRON

AB

## GMWIN

Inverter

AB, OMRON PLC (Master)

GM 6 (Slave)

GM 4 (Slave)

# PWR

# CPU

# DeviceNet

# OUT

# IN

GLOFA I/O module

DeviceNet

Other maker’s I/O module

DeviceNet

Configurator

GLOFA I/O module

Other maker’s I/O module

G4L-DUEA

## ADDRESS

### (10

### (1

MODE

G4L-DUEA

Connector

# PWR

# CPU

# DeviceNet

# OUT

# IN

OMRON

AB

Mode setting switch (Baudrate, Master/Slave)

## GMWIN

NS

MS

| LED Lamp |
| --- |
| MS | Display I/F status of module |
| NS | Display network status of module |

PMU

GM 6 (Slave)

GM 4 (Master)

# PWR

# CPU

# DeviceNet

# OUT

# IN

DeviceNet

Station no. setting switch

| LED Display |
| --- |
| 7-Seg. | Display status of module |

G6L-DUEA

## ADDRESS

### (10

### (1

MODE

MS NS

G6L-DUEA

| LED Lamp |
| --- |
| MS | Display I/F status of module |
| NS | Display network status of module |

Connector

Mode setting switch (Baudrate, Master/Slave)

Station no. setting switch

G0L-DSIA

x 10

(

(     (  (       (

INPUT

DC 24V

24G

24V

.

.      9    11    13    15

NC   1     3     5    7

COM1  8     10    12    14  COM2

NC   0     2      4     6

MS

ADDRESS

Off

On

MODE

NS

PWR

x 1

(

G0L-DSQA

x 10

(

(     (  (       (

INPUT

DC 24V

24G

24V

COM4

COM3  12    13    14    15

NC   8     9    10    11

COM1  4     5     6     7   COM2

NC   0     1      2     3

MS

ADDRESS

Off

On

MODE

NS

PWR

x 1

(

ON

4  3  2  1

ON

4  3  2  1

PWR

GM4 CPU

# DeviceNet

# IN

Out 16

Out 16

Ethernet

TAB (6 Port)

PWR

GM6 CPU

G0L-DSQA

Out 16

Out 16

# DeviceNet

# IN

AB Flex I/O

(1794-ADN / 1794-0816 / 1794-1816)

00 Station

(Master)

01 Station

(Slave)

02 Station

(Slave)

03 Station

(Slave)

00 Station

(Master)

PWR

GM4 CPU

Ethernet

Out 16

Out 16

# DeviceNet

# IN

03 Station

(Slave)

02 Station

(Slave)

01 Station

(Slave)

%MW0

G0L-DSQA

PWR

GM6 CPU

Out 16

Out 16

# DeviceNet

# IN

%MW1

%MW2

%QW0.2.0

%MW0

%QW0.1.0

%QW0.3.0

Only

Available

Not support

yet

In the unit of Byte

Master → Slave 1 (Remote)

Master → Slave 2 (Remote)

Slave 1 (Remote) → Master

In the unit of Byte

Master PLC’s Area

Master PLC’s Area

In case of setting the parameter at slave station,

This station No. means Self station no. (Station no. of GM6)

Slave 1 (Remote) → Master

High speed link

Parameter

High speed link

Parameter